## Slide 1
IEEE SASC RWG: Interferometric and 3D Imaging SAR Sub-Group
April 10, 2023
Raghu G. Raj
United States DEVCOM Army Research Laboratory
Kumar Vijay Mishra
United States Naval Research Laboratory

## Slide 2
3D and Interferometric SAR Sub-group
Chair: Dr. Raghu G. Raj (NRL)
Co-chair: Dr. Kumar Vijay Mishra (ARL)
*No longer active or have not joined any sub-group
Members:
Bradley Evans (UNM) bradleyevans@unm.edu
Stefano Tebaldini (Politecnico di Milano) stefano.tebaldini@polimi.it
Peter Vouras (DoD) synthetic_aperture_twg@ieee.org
Daniel Kamoun (Brandeis) danielkamoun@gmail.com
Enrique
Chad Knight (SDL) Chad.Knight@sdl.usu.edu

## Slide 3
Some Trade-offs
Trades and Rules-of-thumb involved in Across-track Interferometry:
  Correction due to flat earth: Heuristics for selection of reference point
  Multilook operation to improve phase noise vs. Loss in spatial resolution
  Trades involves in sensitivity of phase measurement w.r.t. height estimation
    Maximize baseline separation for higher sensitivity vs. Minimize baseline separation for reduced baseline decorrelation and to prevent height ambiguities due to phase wrapping
Trades and Rules-of-thumb involved in Along-track Interferometry
  Phase correction due to topographic component
  Phase correction due to atmospheric component
  Phase noise correction
Trades and Rules-of-thumb Multi-baseline Interferometry:
  Multi-baseline Across-track: Adaptation of baseline based on the terrain being imaged. Fusion of multiple baselines for the same region.
  Multi-baseline Along-track: Precise estimation of velocity spectrum associated with each pixel in the image.
  Hybrid across-along track: Allows for height estimation of moving targets by combining across- and along- track baselines.
Resolution of SAR image:
  Across-track interferometry w.r.t. system parameters
  Along-track interferometry w.r.t. system parameters

## Slide 4
Applications
3D Imaging
  Algorithms for 3D-SAR Imaging
    Multi-baseline Across-track Imaging (3D InSAR, 3D Stereo SAR)
    3D Tomographic Imaging: Ray and Diffraction tomography
    Volumetric SAR Imaging: linear, curvilinear, flat/curved surface, volume-based (circular, cylindrical, spiral, spherical) SAs
  Algorithms for 3D-ISAR Imaging
    Multi-baseline Across-track/Along-track Imaging (3D InISAR)
    3D Polar-reformatting approach
    Single sensor-based approaches: Scatterer tracking
  Note: Modulo trade-offs, interferometric approaches to 3D imaging yield best reconstruction quality
Algorithms for Velocity measurement
  Multichannel interferometry
  Velocity SAR

## Slide 5
Algorithm Standard Template
Use case: SAR, ISAR, InSAR etc.
Systems attributes:
  Ground-based
  Airborne
  Spaceborne
Algorithm attributes
  Wave-field model: Fresnel, Huygens, near-field, far-field
  Wave approximation
  Processing domain: Time, space, frequency, wavenumber or their combinations
  Signal processing model: discrete time transmit signal, continuous time transmit signal, channel model (including clutter), continuous time receive signal, discrete time receive signal, receive signal processing
  Motion compensation
  Clutter, Inference and Noise
  Rules of thumb
Algorithm parameters:
  Bandwidth
  Beamwidth
  Dwelltime
  Block vs single pixel processing
  Batch vs. Sequential processing
The impact of algorithm attributes and parameters on resolution etc.

## Slide 6
Volunteers?
3D Imaging
  Algorithms for 3D-SAR Imaging
    Multi-baseline Across-track Imaging (3D InSAR, 3D Stereo SAR) (volunteer: Enrique?)
    3D Tomographic Imaging: Ray and Diffraction tomography (volunteer: Vijay, ray or diff)
    Volumetric SAR Imaging: linear, curvilinear, flat/curved surface, volume-based (circular, cylindrical, spiral, spherical) SAs
  Algorithms for 3D-ISAR Imaging
    Multi-baseline Across-track/Along-track Imaging (3D InISAR) (volunteer: Enrique, Raghu)
    3D Polar-reformatting approach (volunteer: Enrique?)
    Single sensor-based approaches: Scatterer tracking
Algorithms for Velocity measurement (volunteer: Raghu)
  Multichannel interferometry
  Velocity SAR
NEED MORE VOLUNTEERS!

## Slide 7
IEEE Std 2450-2019 - IEEE Approved Draft Standard for the Performance of Down-the-Road Radar Used in Traffic Speed Measurements:
IEEE Std 1502-2020 - IEEE Draft Recommended Practice for Radar Cross-Section Test Procedures:
521-2019 - IEEE Standard Letter Designations for Radar-Frequency Bands: https://ieeexplore.ieee.org/document/9027205
1502 - IEEE Recommended Practice for Radar Cross-Section Test Procedures:
1672 - IEEE Standard for Ultrawideband Radar Definitions:
P149/D10, May 2021 - IEEE Draft Recommended Practice for Antenna Measurements: https://ieeexplore.ieee.org/document/9451886
Examples of Writing Radar Standards